## Slide 1: A Bridge to Broader IoT Ecosystems
ETSI IoT Week
Sophia Antipolis, France, Oct 2017

## Slide 2: Where is the value potential of the IoT?
Chart: 
| Home | Offices | Factories | Retail | Worksites | Health | Outside | Cities | Vehicles
Sales | 200 | 70 | 1200 | 410 | 160 | 170 | 560 | 930 | 210
Outside – logistics and navigation $560B to $850B
Factories – operations and equipment optimisation $1.2T to $3.7T
Retail $170B to $1.6T
Health & Fitness $200B to $350B
Home $200B to $350B
Worksites $160B to $930B
Offices $70B to $150B
Aggregated value - $3.9 trillion to $11.1 trillion per year in 2025
Interoperability is required to capture 40% of total value
Less than 1% of data is currently used, mostly for alarms or real-time control
  More can be used for optimisation and prediction
Twice as much value from B2B applications than from consumer
40% of value in developing countries, 60% in developed countries
McKinsey, June 2015 – “The Internet of Things: mapping the value beyond the hype”
  Cities – public health and transportation $930B to $1.7T
Vehicles $210B to $740B
Most of the potential value is in the data and value added services rather than the IoT devices and IoT communication technologies.
  Open standards are needed to overcome fragmentation, connect the silos and unlock the network effect for exponential growth
Notes: value hides in the data and services, the way to capture the value is interoperability
Overcoming barriers to interoperability
  Many choices for communication technologies and standards
  Lack of shared approaches to interoperability
  Existing IoT standards focus on particular technologies and use cases
  This makes it challenging (hard, expensive, risky) to create services across a heterogeneous set of technologies and standards

## Slide 3: Problem: Application/Platform Silos
Internet of Things
IEEE 802.15.4
Ethernet
Bluetooth
Wi-Fi
LoRa
…
: Connectivity
…
Notes: Open standards are not sufficient, the interoperability between them are indispensable.
The problem space that WoT is addressing is the fragmented silos of IoT ecosystems, where too many choices exist when it comes to the IoT technologies and standards.
Although some standards like oneM2M are trying to provide interworking means in technology specific ways, there is still a need and room for common means of interworking especially at the semantic level.
  Non-interoperable cloud platforms that lock you into their platform
  It’s hard to create services that span multiple IoT technologies and standards
Open standards are needed to overcome fragmentation, connect the silos and unlock the network effect for exponential growth
This needs to happen in a way that complements work in IoT alliances and standards development organizations
We know oneM2M is also trying to interconnect with different ecosystems, WoT may provide a useful tool for that.

## Slide 4: W3C WoT Mission
…
Extend Web technologies to the IoT to complement IoT standards by being descriptive instead of prescriptive
Web of Things: “glue in-between”
Not to be yet another standard
Notes: WoT is not like other IoT standards that try to define specific ways of communicating and interaction (e.g. interfaces, protocols, primitives), rather, it provides a tool set to be able to describe what those interfaces are, and how to interact.
W3C’s Value Proposition:
Our standards are critical for Web browsers and semantic technologies for linked data
  Semantic technologies have huge importance for the IoT
The Web of Things as a means for simplifying application development and enabling integration across devices from different vendors and using different technology stacks, e.g.
  Apple HomeKit, Android Things, OCF, oneM2M, OPC, LPWAN, Bluetooth, …

## Slide 5: W3C WoT Scope
…
WoT: cross-platform, cross-domain
Notes: The vision is to support cross-xx interoperability, and bridge the ecosystems in a harmonized way.

## Slide 6: Where is WoT Positioned?
Web of Things: Application Layer
Internet of Things
IEEE 802.15.4
Ethernet
Bluetooth
Wi-Fi
LoRa
…
: Connectivity
Notes: let’s say above IP layer, describing the transport means and data model (interaction pattern)

## Slide 7: W3C WoT Approach
Platform B
Platform API
Application
Data Model
Protocol
Re-usable Technological Building Blocks
easy integration across platforms
Semantic
Metadata
Platform A
Platform API
Application
Data Model
Protocol
describe Thing
complement
learn how to interact with Thing
“WoT Interface”
Notes: the services a producing-thing exposes can be described in semantic metadata so that the consuming thing can understand and learn to interact with.

## Slide 8: W3C WoT Building Blocks
Lua
OCF
WoT Servient
Runtime Environment
Thing Description
WoT Scripting API for browser-like runtime environment
WoT Binding Templates to connect to different platforms and ecosystems
WoT Thing Description (TD) with simple interaction model
Events
Properties
Actions
Interaction Model
Binding Templates
Scripting API
App Script 2
Server
Client
App Script 1
Expose
Consume
Local Hardware
HTTP
CoAP
OneM2M
JavaScript
BACnet
Things can be in client and/or server role: “Servient”
…
Notes: WoT Thing Description (TD)
  Machine-understandable format
  Uniform documentation
  Linked Data vocabularies
    Simple interaction model
    Generic data model (JSON-like)
    Semantic Web ontology
  Extension points
    Domain-specific vocabularies
    New interaction patterns
  Multiple serializations
    JSON-LD (first CR release)
    JSON, CBOR, EXI, …
WoT Binding Templates
  Descriptions for specific protocols and platforms
  Used in Thing Description
  Re-usable binding “drivers”
WoT Scripting API
  Browser-like runtime for platform-independent IoT applications

## Slide 9: JSON-LD Serialization
{
"@context": [
"http://w3c.github.io/wot/w3c-wot-td-context.jsonld",
{ "domain": "http://example.org/actuator#" }
],
"@type": "Thing",
"name": "MyLEDThing",
"security": {
"cat": "token:jwt",
"alg": "HS256",
"as": "https://authority-issuing.example.org"
},
"interaction": [
{ "@type": ["Action", "domain:fadeIn"],
"name": "fadeIn",
"inputData": {
"type": "integer",
"minimum": "0",
"domain:unit": "domain:ms"
},
"link": [
{ "href": "coaps://myled.example.com:5684/in",
"mediaType": "application/exi",
"REST:method": "POST"
},
{ "href": "https://mytemp.example.com:8080/in",
"mediaType": "application/json",
"REST:method": "POST"
}
]
},
{
"@type": ["Action", "domain:fadeOut"],
"name": "fadeOut",
"inputData": {
"valueType": {"type": "integer"},
"domain:unit": "domain:ms"
},
"links": [
{
"href": "out",
"mediaType": "application/exi"
},
{
"href": "https://mytemp.example.com:8080/out",
"mediaType": "application/json"
}
]
},
{
"@type": ["Event", "domain:alert"],
"name": "criticalCondition",
"outputData": {"valueType": {"type": "string"}},
"links": [
{
"href": "ev",
"mediaType": "application/exi"
}
]
}
]
}
Linked Data
domain-specific vocabulary
JSON Schema base types plus semantics
W3C WoT TD vocabulary
protocol binding specifics

## Slide 10: Things as Objects with Descriptions
Application Script that abstracts the device as a Thing
Produced Thing as software object
Consumed Thing as software object
Application Script that interacts with a consumed Thing
Properties
Events
Actions
Properties
Events
Actions
Synchronisation across the Internet using Web protocols
Device
Sensors and actuators
IoT technology standard
Thing Description
Application publishes
Every Thing has a URL that identifies the Thing, and links to its description.
The URL is used as an RDF node for semantic descriptions of Things and their relationships
RDF: knowledge representation using binary graphs with labelled links between RDF nodes
Application platforms use Thing Descriptions to automatically create the objects for exposed and consumed Things
exposes
consumes

## Slide 11: W3C WoT Architecture Patterns
Thing
Direct Thing-to-Thing
Interaction
Interaction Model
Classic Firmware
Protocol
Existing Device
Complement Existing Devices
+
Thing

Thing
Interaction Model
Scripting API
App Script
Protocol
Gateway
Servient
Interaction Model
Binding Templates
Scripting API
Proxy Thing
Orchestr. Client
Virtual Thing
Cloud
Servient
Interaction Model
Binding Templates
Scripting API
Digital Twiin
Orchestr. Client
Digital Twiin
Web Browser
Web Integration
Interaction Model
Scripting API
App Script
Binding Templates

## Slide 12: W3C WoT Process
Interest Group (IG)
Started spring 2015
199 participants
Informal work, outreach
Explorative work, validation
PlugFests with running code
Liaisons and collaborations with other organizations and SDOs (+ “OpenDays”)
Working Group (WG)
Started December 2016
100 participants
Normative standardization
Work on deliverables
W3C Patent Policy for royalty-free standards
Member organizations and Invited Experts
https://www.w3.org/2016/07/wot-ig-charter.html
https://www.w3.org/2016/12/wot-wg-2016.html

## Slide 13: W3C WoT Progress
2014: Stakeholders identified at W3C Workshop
2015: IG started to identify initial building blocks
  Current Practices documented (http://w3c.github.io/wot/current-practices/wot-practices.html)
  Practical evaluation in “PlugFests”
2016/17: WG chartered until end of 2018
  Editor’s Drafts available
  3 First Public Working Drafts published in Sep. 2017
  Candidate Recommendations end of 2018…
2019: WG re-chartering for next building blocks
  IG is continuously exploring and identifying

## Slide 14: W3C WoT Online Resources
W3C WoT Wiki (IG+WG organizational information)
  https://www.w3.org/WoT/IG/wiki/Main_Page
W3C WoT Interest Group
  https://www.w3.org/2016/07/wot-ig-charter.html (charter)
  https://lists.w3.org/Archives/Public/public-wot-ig/ (subscribe to mailing list)
  https://github.com/w3c/wot (technical proposals)
W3C WoT Working Group
  https://www.w3.org/2016/12/wot-wg-2016.html (charter)
  https://www.w3.org/WoT/WG/ (dashboard)
W3C WoT Editor’s Drafts
  https://w3c.github.io/wot-architecture/
  https://w3c.github.io/wot-thing-description/
  https://w3c.github.io/wot-scripting-api/
  https://w3c.github.io/wot-binding-templates/
FPWD!
FPWD!
FPWD!

## Slide 15: Opportunities for Reuse/Integration
Royalty-free Web standards
Technological building blocks
  Non-prescriptive: take what you need
  Open source reference implementation https://github.com/thingweb/node-wot
Extension points
  Semantic vocabulary  iot.schema.org, oneM2M, …
  Binding Templates  Web, CoRE, OCF, oneM2M, …
  Libraries on top of Scripting API  individual Members

## Slide 16: W3C WoT Liaisons
Active
  OCF
  OneM2M
  OPC Foundation
Potential
  OpenFog
  OMA LWM2M / IPSO Alliance
  EchoNet
  Fairhair Alliance

## Slide 17: W3C - oneM2M Collaboration
Common ground of Semantic Interoperability for IoT
  Standards, tools and expertise on Semantic Web (RDF/OWL/SPARQL) as the building blocks of oneM2M semantic features (ontology management, semantic query/discovery, …)
    Importance of machine interpretable descriptions rather than relying on informal documentation that may diverge over time
    Discovering Things based upon their capabilities and context of use
    Inferring knowledge of Things and environments
    Designing compositions of services that can be proven to interoperate
    Addressing inevitability of change, especially across uncoupled or weakly coupled communities
  Well-aligned semantic models between WoT and oneM2M Base Ontology and Smart Device Template as the solid base of interoperability (see next pages)
Ongoing Work Item “oneM2M-WoT Interworking”
Notes: both organizations have recognized the importance of semantic technology for the IoT interoperability. Especially useful to make machines/things to understand each other with normalized machine languages.
W3C’s suite of standards for semantic technologies and linked data
Importance of machine interpretable descriptions rather than relying on informal documentation that may diverge over time
Discovering things based upon their capabilities and context of use
Adaptation of user interfaces and application logic to match a chosen device or service
Designing compositions of services that can be proven to interoperate
Balancing expressivity with complexity given different requirements
Challenges in addressing inevitability of change, especially across uncoupled or weakly coupled communities
Tuning standardisation processes to the needs of vocabulary development
Opportunities for collaboration?

## Slide 18: Well-aligned base of Semantic Interoperability
The core concepts in each model are well mapped.
WoT TD & oneM2M BO Mapping
The WoT TD Core Model

## Slide 19: Well-aligned base of Semantic Interoperability
Event more direct mapping observed.
WoT TD & oneM2M/HGI SDT Mapping
The WoT TD Core Model
oneM2M SDT

## Slide 20: Added value of WoT to oneM2M
A descriptive & semantic framework (TD) bridging with many other IoT ecosystems in an easier way
A close and natural engagement with Web developers who are more familiar with Web technologies like the Scripting API
Device Ecosystems
Web developers
TD
Scripting API

## Slide 21: Bridging to Broader IoT Ecosystems
Exposing the “WoT i/f” to oneM2M systems
  WoT services/data (described in WoT TD) can be consumed by oneM2M applications
  oneM2M IPE design can be simplified based on the common description of TD (works as BO but more generic)
Actuator
CSE
“WoT i/f”
Inter-working Proxy (AE)
Mca
oneM2M Application (AE)
Mca
Sensor
“WoT i/f”
Inter-working Proxy (AE)
Mca
MN
CSE
Mcc
Infrastructure Node
Thing Description
encapsulate & map
uses
provides
uses
oneM2M Resource Model
WoT TD
mapping
uses
provides

## Slide 22: Bridging to Broader IoT Ecosystems
Exposing the oneM2M i/f to WoT-compatible systems
  oneM2M services/data can be consumed by WoT Servients (as if they “speak” oneM2M protocol according to TD )
  oneM2M protocol bindings can be described in a machine-understandable way using WoT TD Binding Template (automated interworking becomes possible)
WoT Servient
Interaction Model
Binding Templates
Application(s)
Logic + Data
Cient
WoT Servient
Interaction Model
Binding Templates
Links (URIs), Metadata
Server
Client
Server
Thing Description

## Slide 23: Take-away
WoT is not yet another prescriptive standard but a descriptive tool for bridging the IoT ecosystems
TD is the heart of WoT
Common ground of semantic interoperability shows promising interworking solution between WoT and oneM2M
Work to be further progressed on both sides via closer collaboration

## Slide 24: Thank you!!!