## Slide 1: OneDM@WoT Plugfest
Summary
March 24, 2021
Michael J. Koster

## Slide 2: Goals
Explore SDF => TM/TD Generation
Define how semantic annotation from SDF works
Test the Modbus protocol binding

## Slide 3: EHD Propulsion Experiment "Ionic Wind Tunnel"
DC Power Supply
DC-DC Step-up Conv
Mobile Dielectric
V
F
A
RTU
Uhv
Ihv
Thrust (load cell)
EHD Thruster
Modbus Control
Ref: https://www.researchgate.net/publication/235189622_A_Model_of_an_Ideal_Electrohydrodynamic_Thruster
+++++++++++
-----------
Notes: Ionic paddle wheel:
Through special arrangement of the electrodes, a strong electric field is created at the anode, which "steals" electrical charges from the Nitrogen molecules, making them positive ions. The N2(+) ions then drift toward the cathode due to electrostatic attraction, where along the way they statistically interact with air molecules and transfer momentum to them, generating a thrust force roughly in the plane of the electrodes, in accordance with Newton's third law of motion. The circuit is completed by the N2(+) ions arriving at the cathode, where they collect the stolen charge and become neutral molecules again. The current in the circuit is an indication of the ionic flow density when operating in the non-arcing condition.

## Slide 4: Modbus Integration Test Case
SDF
MB Bind
MB TM
MB TD
?
node-wot Client
node-wot Application
Modbus Proxy
SDF2TM
Consume
DC Power Supply
RTU
Modbus+TCP
Configuration Time
Modbus RTU
PHY
EM
Code Gen

## Slide 5: Model Construction Workflow
SDF Thing
SDF Object
SDF Object
SDF Object
SDF Object
sdfRef
TD DS & Forms
WoT TM/TD
SDF2TD
Instance Binding

## Slide 6: SDF to TM Conversion Workflow
Inserted WoT DataSchema and Forms construct into SDF as extensions
Created an sdfThing that customizes its sdfObject components and inserts the WoT extensions:
https://github.com/mjkoster/onefb-sdk/blob/main/control-models/modbus/sdfthing-modbus-ehd-rtu.sdf.json
Generated a TD manually from the SDF file:
https://github.com/mjkoster/onefb-sdk/blob/main/control-models/modbus/modbus-rtu.td.jsonld
TBD Create a set of transformation rules/handlers for creating TD from SDF Thing
Extend the conversion tool and framework
  Read Input => Invoke Transforms => Write Output

## Slide 7: Semantic Annotation using SDF
SDF URIs have json-pointer fragments
application/sdf+json contentType needs to be indicated where SDF is referenced
"@type": {
"https://onedm.org/playground/#/sdfObject/Voltage",
"contentType": "application/sdf+json"
}
Semantic annotation for sdfObjects using "links" construct in the TD, since there is no TD Object class
  We need a link relation like "implements" to describe this pattern

## Slide 8: sdf conversion gaps
SDF1.1 changes
  New pattern for input and output, JSON object
  JSON Schema required for input and output elements
  sdfChoice + mapping for enum generation
Generate composed TD
  Working with composed SDF Thing => TD
  Add annotation to the generated TD based on SDF source references

## Slide 9: TD Vocabulary – value scaling
We need to represent the data pattern which encodes a fixed point decimal number using an integer
Also other similar use cases where a linear re-scaling is needed
scaleMinimum and scaleMaximum will be deprecated in SDF 1.1
digitalMinimum, digitalMaximum proposed as instance/protocol binding to describe the encoding
unit, minimum, maximum, and multipleOf will be for the modeled engineering values

## Slide 10: Modbus binding
Hosted 2 modbus devices for the test case and plugfest
Modbus vocabulary suggestions
  use address and quantity instead of offset and length
  review "entity" concept to collapse read/write/obs
Modbus URI construction feedback
Modbus requires read multiple entities
  Should we use array property or TD readmultiple?
  Entity blocks need to be defined separately in the TD
  Entity size needs to be defined in a dataschema extension
  How do we semantically identify the individual entities?

## Slide 11: Backup
Example node-RED application
Mapping file and binding extensions to SDF
Semantic Proxy

## Slide 12: Example application using Node-RED
Sequences the power supply output voltage control through a series of steps and records the electrode voltage, electrode current, and thrust
Value scaling reflected in TD extension parameters
Setup parameters for maximum voltage and current, DC voltage step, and step time
Start button is an example of a long-running action (if the experiment had its own TD)

## Slide 13: Mapping Files, Bindings, and Extension Points
Examples of extension points based on auxiliary schemas
  DataSchema, ProtocolBinding, Hyperlink
Declaration Format - "extensionPoint" in info block
How to identify points in the base schema that the extension point is valid for

## Slide 14: Extension Declaration Format
"extensionPoint": {
"DataSchema" : {
"description": "Additional data schema constraints and mappings",
"sdfRef": "#/sdfExtensionSchema/DataSchema"
},
"ProtocolBinding": {
"description": "Protocol Binding Form compatible with WoT TD Form",
"sdfRef": "#/sdfExtensionSchema/ProtocolBinding"
}
"sdfAction": {
"SetAmperage": {
"sdfInputData":{
"sdfRef": "#/sdfThing/DCPowerSupply_LW3010E/sdfData/AmperageData",
"DataSchema": {
"WidthInBits": 16
}
},
"ProtocolBinding": {
"href": "tcp+modbus://192.168.1.1:502/",
"modv:unitID": 1,
"modv:regID": 1001,
"modv:function": "WriteHoldingRegister"
}

## Slide 15: Semantic Proxy
SDF
OCFMap
OMA Map
OCF TM
OMA TM
OCF TD
OMA TD
OMA MOD
OCF OAS
OCF Conversion
OMA Conversion
SDF2TM
?
node-wot Proxy
OCF Client
OMA Server
SDF2TM
?
Consume
Expose