## Slide 1: WoT Profiles
Michael Lagally
22 June 2021

## Slide 2: Agenda
Introduction to WoT profiles
Actions
HTTP Protocol Binding
Events
PRs
Test Plan (Not discussed)

## Slide 3: What is a WoT profile?
A WoT Profile is a normative subset of a WoT Thing Description with a normative binding to a selected protocol.
Profiles guarantee interoperability between compliant implementations, multiple profiles are possible.
The WoT Profile Specification defines a normative set of constraints and rules on the data model, representation format and protocol binding.
These constraints and rules set limitations and make decisions that reduce the complexity for implementers of the WoT standard.
The rules are prescriptive, to ensure that compliant implementations satisfy the semantic guarantees implied by them.

## Slide 4: Constraints:
Constraints on | Rationale | Example
vocabulary of Thing Description classes | guaranteed set of metadata fields | Make specific vocabulary terms mandatory, remove others
class relationships | unambiguous structure | limited cardinality, e.g. only one form per operation per interaction affordance.
values of vocabulary terms | simplified processing | Limit the length of characters per string. Always use arrays, where the spec permits a string or an array of strings.
data schemas | simplified processing | Limits on nested objects or arrays of arrays
security | reduced implementation effort | Only a restricted set of security mechanisms
protocol binding | guaranteed protocol semantics | limited protocol(s) and protocol features, Example: predefined mapping of http verbs (GET/PUT) to operation verbs, similar constraints for other protocols.

## Slide 5: What are we currently doing?
Defining a core/baseline profile with a HTTP binding.
Identifying constraints and rules on the data model.
Unambiguous interaction semantics for properties, actions and events.
Constraints on payload formats.
Protocol binding semantics, e.g. headers, response codes.
Best practice security requirements.
Representation (TD Serialisation) format constraints.

## Slide 6: Actions

## Slide 7: Actions
The server models interactions that cause state change via actions.
Actions can have a different request modes, they can be synchronous or asynchronous.
The TD does not have a mechanism to annotate whether an action is sync or async. Synchronous action invocations return (after a while) with a response (result or timeout) when it is complete. ., [the actual operation (e.g. robot arm moving) may still be ongoing.]
Asynchronous actions are triggered by the invocation, they return instantaneously with a response.
This response may contain various data, a handle, an id, invocation status.
The consumer should be able to indicate, whether he wants to wait (sync call with a timeout) or if he wants to perform an async call.

## Slide 8: Request modes and timeout
The request mode can be specified with query parameters "iot.sync" or "iot.async".
By default if none of the parameters is set then the request is asynchronous.
These parameters must not be set both.
The asynchronous mode is a preferrable way of doing invocation as it does not consume as much server resources as compared with the synchronous mode.
Optionally, a timeout value in milliseconds may be provided with the "iot.timeout" query parameter.

## Slide 9: Request modes and timeout
Discussion: we could use mode= “sync/async, potential future extensions. There may be implementations that only can be sync or async. Suggested approach: we force the producer to support both ways. A server could indicate that it does not support sync calls, this could be indicated via a response code producer should define whether it is sync or async consumer code for sync and async is very different hard real time is not a goal here, focus is green field sync does not mean that the scripting API needs to be synchronous, the script is still async we could make all actions async and meet the goals of the charter period TD annotations for sync/async are planned per issue https://github.com/w3c/wot-thing-description/issues/890 initiate, monitor and cancel are on the charter – let’s not defer defining basic actions to a future spec but address it in the profile defining sync / async is easy, however there are several issues that require more thought – defer to 2.0 we should clarify actions based on actual use cases, these were done in Plugfest by various companies, Echonet binding should be considered

## Slide 10: HTTP Protocol Binding

## Slide 11: HTTP Protocol binding Methods, Response codes, Headers, Payloads
Methods
Prohibit all unused methods, e.g. HEAD, CONNECT, …
Discussion: Are directories profile compliant, they use “head” in some cases. For now exclude directories from profile considerations.
Response Codes
An initial list of HTTP response codes has been defined recently.
Additional codes / clarifiations may be required.

## Slide 12: HTTP Protocol binding Methods, Response codes, Headers, Payloads
Headers
We have to select/define specific HTTP header fields wrt. content formats, timeouts etc.
Content Type / Content Coding Formats
JSON, XML, Binary?
Discussion: Start with only JSON, all binary data (e.g. jpeg and png images?) would be base64 encoded exclude XML, CBOR for now video streams etc. would be problematic use cases, we would be returning URLs but not streams
Links to html pages, video streams, … are permitted, we are not constraining link targets
We are not constraining video formats, but it is up to the consumer to interpret the format
We could reuse MPEG-DASH, Netflix, … formats, could ask media experts for their opinion Video streams are out of scope of the core profile
Do we select different data formats for media? No

## Slide 13: Events

## Slide 14: Invent or align
Consider alignment with standardised Cloud Events
https://cloudevents.io/
https://github.com/cloudevents
Discussion:
Todo: check IP policy of Cloud Events
Also OpenAPI could offer an event model we could adopt See also https://github.com/w3c/wot-thing-description/issues/893
We could adopt SSE, since there’s now wider support in browsers

## Slide 15: PRs

## Slide 16: PRs
RFC 2119 markup: add css mark <span> into index.html
https://github.com/w3c/wot-profile/pull/79
Discussion:
We noticed that some span markups are in editors notes – these need to be cleaned up in a further iteration.
We merged the PR, Mizushima-san will provide additional comments.
McCool will do another pass using the test tooling.

## Slide 17: References
WoT Architecture task force
  https://www.w3.org/WoT/activities/tf-architecture/
WoT Profile repository
  https://github.com/w3c/wot-profile
Working draft:
  https://www.w3.org/TR/wot-profile/