## Slide 1: W3C Web of Things (WoT) Update
Michael McCool
June 2021

## Slide 2: W3C Web of Things (WoT)
W3C WoT Working Group goal: Adapting web technologies to IoT
Published: Thing Description (TD) metadata format
  TD describes the available interactions (network API) of a Thing
In Progress: TD 1.1 Update, Thing Models, Discovery, Profiles
  How to obtain TDs? How to ensure interoperability?
App
App
App
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV
App
App
App
{ properties, actions, events }
WoT API
WoT API
WoT API
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV

## Slide 3: WoT Thing Descriptions
{
"@context": [
"https://www.w3.org/ns/td",
{ "iot": "http://iotschema.org/" }
],
"id": "urn:dev:ops:32473-WoTLamp-1234",
"title": "MyLEDThing",
"description": "RGB LED torchiere",
"@type": ["Thing", "iot:Light"],
"securityDefinitions": ["default": {
"scheme": "bearer"
}],
"security": ["default"],
"properties": {
"brightness": {
"@type": ["iot:Brightness"],
"type": "integer",
"minimum": 0,
"maximum": 100,
"forms": [ ... ]
}
},
"actions": {
"fadeIn": {
...
Door = Thing
Handle = Affordance
What?
How?
Open
Pull
Turn
  WHAT the possible choices are
    Properties
    Events
    Actions
  HOW to interact with the Thing
    Protocol operations and options
    Data schemas and content types
    Security requirements

## Slide 4: Usage Patterns

## Slide 5: Current WoT WG Charter Work Items
Architectural Requirements, Use Cases, and Vocabulary
  Understand and state requirements for new use cases, architectural patterns, and concepts.
Link Relation Types:
  Definition of specific link relation types for specific relationships.
Observe Defaults:
  For protocols such as HTTP where multiple ways to implement "observe" is possible, define a default.
Implementation View Spec:
  More fully define details of implementations.
Interoperability Profiles:
  Support plug-and-play interoperabilty via a profile mechanism
  Define profiles that allow for finite implementability
Thing Models:
  Define how Thing Descriptions can defined in a modular way.
Complex Interactions:
  Document how complex interactions can be supported via hypermedia controls.
Discovery:
  Define how Things are discovered in both local and global contexts and Thing Descriptions are distributed.
Identifier Management:
  Mitigate privacy risks by defining how identifiers are managed and updated.
Security Schemes:
  Vocabulary for new security schemes supporting targeted protocols and use cases.
Thing Description Vocabulary:
  Extensions to Thing Description vocabulary definitions.
Protocol Vocabulary and Bindings:
  Extensions to protocol vocabulary definitions and protocol bindings.

## Slide 6: New Deliverables
Thing Description 1.1
  Canonicalization (and WIP, Signing)
  Validation levels
  Thing Model
  various other extensions, e.g. to security, data schemas, etc.
Discovery
  Introductions: DNS-SD, DID, CoRE RD
  Directory Service: HTTP API for searchable database of TDs
  Self-Description: .well-known, fetching of TD directly from Things
Profiles
  Emphasis on "hub" use-case, http/json
Use Cases and Requirements (informative document)

## Slide 7: Thing Description 1.1: Updates
Canonicalization and Signing
  WIP, but proposal is based on JOSE/JWS/JWA (incl. RFC 8037)
  Can extract parts of a TD to sign using JSONPointer/JSONPath/XPath queries
Security Scheme Improvements
  URI Templates
  Security information in body
  OAuth "device" flow
Thing Model
  TD describes instance, TM describes class
  Provides templating/parameterization mechanism
  TD can reference one TM using a link
  TMs can reference or extend other TMs (and parts of other TMs)

## Slide 8: Discovery: Goals
Capabilities
  Support both local and global/remote discovery (unconstrained by network domain)
  Support "localizable" discovery (constrainable by location)
  Support both "syntactic query" (keywords) and "semantic query" (linked data)
  Support a directory service for searching large repositories of Things
  Support peer-to-peer (self-identifying "smart object") discovery
Privacy-Preserving Architecture
  Respect device and information Lifecycle
  Distribute TDs only to authenticated and authorized users
  Don’t leak private data to unauthorized users
  Don’t leak data that can be used to INFER private information to unauthorized users
Alignment with Existing and Evolving Standards
  IETF CoRE Resource Directories, CoRE Link Format, DID, OGC, WGS84, XPath, …
  Compatible with WoT Scripting API

## Slide 9: Discovery: Two-Phase Architecture
Phase 1: Introduction
  “First Contact” Protocol
    Answers the question: How to initiate discovery from zero knowledge?
  Open
    Can be accessed with no or limited access controls
    Based on existing standards, and can be extended to new standards
  Lightweight
    Does not use significant resources on responder
    Resistant to Denial of Service attacks
  Provides intentionally limited information
    Avoid leaking any metadata that can be used to infer private data
    This includes types of devices, device ids, owners, timestamps, etc.
Phase 2: Exploration
  Authentication and authorization required
  Supports more complex query and filtering capabilities (JSON Path, XPath, SPARQL)
  Provides access to rich metadata (TDs)
  Access controls can limit data returned

## Slide 10: Discovery: Status
Introductions
  DNS-SD (including mDNS) – new service names
  CoRE RD – resource types
  DID – endpoint types
  Well-known URLs: to "guess" URL from an IP
  Direct: anything else that returns a URL
  Note: link types distinguishing a Directory and a Thing are useful but not mandatory
Exploration
  "Smart Objects": Retrieve TD directly from Thing
  Directory service API: described using a TD
  Provides multiple query types:
    JSONPath – mandatory
    XPath – optional
    SPARQL – optional
  Pagination, etc.

## Slide 11: What is a WoT Profile?
A WoT Profile is a normative subset of a WoT Thing Description with a normative binding to a selected protocol.
Profiles guarantee interoperability between compliant implementations, multiple profiles are possible.
The WoT Profile Specification defines a normative set of constraints and rules on the data model, representation format and protocol binding.
These constraints and rules provide clarifications and make decisions that reduce the complexity for implementers of the WoT standard.
The rules are prescriptive, to ensure that compliant implementations satisfy the semantic guarantees implied by them.

## Slide 12: Profiles: Constraints
Constraints on | Rationale | Example
vocabulary of Thing Description classes | guaranteed set of metadata fields | Make specific vocabulary terms mandatory, remove others
class relationships | unambiguous structure | limited cardinality, e.g. only one form per operation per interaction affordance.
values of vocabulary terms | simplified processing | Limit the length of characters per string. Always use arrays, where the spec permits a string or an array of strings.
data schemas | simplified processing | Limits on nesting
security | reduced implementation effort | Only a restricted set of security mechanisms
protocol binding | guaranteed protocol semantics | limited protocol(s) and protocol features, Example: predefined mapping of http verbs (GET/PUT) to operation verbs, similar constraints for other protocols.

## Slide 13: Profiles: Current Work
Defining a core/baseline profile with a HTTP binding.
Identifying constraints and rules on the data model.
Unambiguous interaction semantics for properties, actions and events.
Constraints on payload formats.
Protocol binding semantics, e.g. headers, response codes.
Security constraints.
Representation format constraints.

## Slide 14: Use Cases: W3C Smart City Workshop
Visitor Guidance
Energy Management
Retail Services
Health
Others
  Law Enforcement
  Parking
  Accessibility
  Traffic and Logistics
  Public Transportation
  Air Quality and Weather
  Cultural Space Mgmt
  Construction Services
  Land Management
  Emergency Services
  Water Management
  Hybrid Ruralization

## Slide 15: WoT Orchestration
Node-RED/node-gen
node-wot/Scripting API
WoTHelpers.fetch( "coap://localhost:5683/counter" ).then( async (td) => {
// using await for serial execution (note 'async' in then() of fetch())
try {
let thing = await WoT.consume(td);
console.info( "=== TD ===" );
console.info(td);
console.info( "==========" );
// read property #1
let read1 = await thing.readProperty( "count" );
console.info( "count value is" , read1);
// increment property #1 (without step)
await thing.invokeAction( "increment" );
let inc1 = await thing.readProperty( "count" );
console.info( "count value after increment #1 is" , inc1);
// increment property #2 (with step)
await thing.invokeAction( "increment" , {'step' : 3});
let inc2 = await thing.readProperty( "count" );
console.info( "count value after increment #2 (with step 3) is" , inc2);
// decrement property
await thing.invokeAction( "decrement" );
let dec1 = await thing.readProperty( "count" );
console.info( "count value after decrement is" , dec1);
} catch(err) {
console.error( "Script error:" , err);
}
}).catch( (err) => { console.error( "Fetch error:" , err); });

## Slide 16: Documents and Resources
New/Updated Normative Documents in Draft Status:
Architecture 1.1: https://github.com/w3c/wot-architecture
Thing Description 1.1: https://github.com/w3c/wot-thing-description
Discovery: https://github.com/w3c/wot-discovery
Profiles: https://github.com/w3c/wot-profile
New/Updated Informative Documents in Draft Status:
Binding Templates: https://github.com/w3c/wot-binding-templates
Scripting API: https://github.com/w3c/wot-scripting-api
Use Cases and Requirements: https://github.com/w3c/wot-usecases
Other Resources:
Web Site: https://www.w3.org/WoT/

## Slide 17: Contacts
Dr. Michael McCool
Principal Engineer
Intel
Technology Pathfinding
michael.mccool@intel.com
Dr. Sebastian Kaebisch
Senior Key Expert
Siemens
Technology
sebastian.kaebisch@siemens.com
https://www.w3.org/WoT

## Slide 18: Backup

## Slide 19: Image Credits
Solar Installation Vietnam: By Intel Free Press - https://www.flickr.com/photos/intelfreepress/7169063498/sizes/o/in/photostream/, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=28011974
Telemedicine Consult: By Intel Free Press - https://www.flickr.com/photos/intelfreepress/6948764580/sizes/o/in/photostream/, CC BY 2.0, https://commons.wikimedia.org/wiki/File:Telemedicine_Consult.jpg