## Slide 1: WoT Summary and Status
Michael McCool
October 2021

## Slide 2: Outline
What is WoT?
  Applying and extending web standards for IoT
  Descriptive interoperability
  Current status of deliverables
Recent Activity
  Plugfest
  Commercial usages
  Discovery/directory implementations
  Relationship to IETF activity
  Items under discussion
  New charters/new deliverables

## Slide 3: W3C Web of Things (WoT)
W3C Working Group goal: Adapting web technologies to IoT
Already published: Thing Description (TD) metadata format
  TD describes the available interactions (network API) of a Thing
New standards work in progress, including Discovery
  How does a potential user obtain the TDs for a Thing?
App
App
App
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV
App
App
App
{ properties, actions, events }
WoT API
WoT API
WoT API
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV

## Slide 4: WoT Descriptive Interoperability
WoT Thing Description (TD)
{
"@context": [
"https://www.w3.org/2019/wot/td/v1",
{ "iot": "http://iotschema.org/" }
],
"id": "urn:dev:org:32473:1234567890",
"title": "MyLEDThing",
"description": "RGB LED torchiere",
"@type": ["Thing", "iot:Light"],
"securityDefinitions": ["default": {
"scheme": "bearer"
}],
"security": ["default"],
"properties": {
"brightness": {
"@type": ["iot:Brightness"],
"type": "integer",
"minimum": 0,
"maximum": 100,
"forms": [ ... ]
}
},
"actions": {
"fadeIn": {
...
Door = Thing
Handle = Affordance
What?
How?
Open
Pull
Turn
WoT Architecture
  Constraints
    Things must have a TD
    Must use hypermedia controls (general WoT)
      URIs, standard set of methods, media types
  Thing Description Affordances
    Describes WHAT the possible choices are
    Describes HOW to interact with the Thing

## Slide 5: Current Status
New/Updated Normative Documents in Draft Status:
Architecture 1.1: https://github.com/w3c/wot-architecture
Thing Description 1.1: https://github.com/w3c/wot-thing-description
Discovery: https://github.com/w3c/wot-discovery
Profiles: https://github.com/w3c/wot-profile
New/Updated Informative Documents in Draft Status:
Binding Templates: https://github.com/w3c/wot-binding-templates
Scripting API: https://github.com/w3c/wot-scripting-api
Use Cases and Requirements: https://github.com/w3c/wot-usecases
Marketing Improvements:
New Web Site, Animation, Resources: https://www.w3.org/WoT/

## Slide 6: Recent Activity
Plugfest
  Projects: https://github.com/w3c/wot-testing/labels/Plugfest%202021.09
New Commercial Usages
  Takenaka Construction – Smart Building Information Management systems
  Netzo – IoT dashboards and device management
Directory Implementations
  WoT Hive, LogiLab (SPARQL based), Fraunhofer LinkSmart
IETF Relationships: JSON Path, CoreRD, COSE/JOSE, ASDF
Under Discussion (IG Notes expected)
  Geospatial data, Embedded JSON Signatures
New Charters/New Deliverables

## Slide 7: Contacts
Dr. Michael McCool
Principal Engineer
Intel
Technology Pathfinding
michael.mccool@intel.com
Dr. Sebastian Kaebisch
Senior Key Expert
Siemens
Technology
sebastian.kaebisch@siemens.com
https://www.w3.org/WoT

## Slide 8: Backup

## Slide 9: Usage Patterns Overview

## Slide 10: WoT Orchestration
Node-RED/node-gen
node-wot/Scripting API
WoTHelpers.fetch( "coap://localhost:5683/counter" ).then( async (td) => {
// using await for serial execution (note 'async' in then() of fetch())
try {
let thing = await WoT.consume(td);
console.info( "=== TD ===" );
console.info(td);
console.info( "==========" );
// read property #1
let read1 = await thing.readProperty( "count" );
console.info( "count value is" , read1);
// increment property #1 (without step)
await thing.invokeAction( "increment" );
let inc1 = await thing.readProperty( "count" );
console.info( "count value after increment #1 is" , inc1);
// increment property #2 (with step)
await thing.invokeAction( "increment" , {'step' : 3});
let inc2 = await thing.readProperty( "count" );
console.info( "count value after increment #2 (with step 3) is" , inc2);
// decrement property
await thing.invokeAction( "decrement" );
let dec1 = await thing.readProperty( "count" );
console.info( "count value after decrement is" , dec1);
} catch(err) {
console.error( "Script error:" , err);
}
}).catch( (err) => { console.error( "Fetch error:" , err); });

## Slide 11: Current WoT WG Charter Work Items
Architectural Requirements, Use Cases, and Vocabulary
  Understand and state requirements for new use cases, architectural patterns, and concepts.
Link Relation Types:
  Definition of specific link relation types for specific relationships.
Observe Defaults:
  For protocols such as HTTP where multiple ways to implement "observe" is possible, define a default.
Implementation View Spec:
  More fully define details of implementations.
Interoperability Profiles:
  Support plug-and-play interoperabilty via a profile mechanism
  Define profiles that allow for finite implementability
Thing Description Templates:
  Define how Thing Descriptions can defined in a modular way.
Complex Interactions:
  Document how complex interactions can be supported via hypermedia controls.
Discovery:
  Define how Things are discovered in both local and global contexts and Thing Descriptions are distributed.
Identifier Management:
  Mitigate privacy risks by defining how identifiers are managed and updated.
Security Schemes:
  Vocabulary for new security schemes supporting targeted protocols and use cases.
Thing Description Vocabulary:
  Extensions to Thing Description vocabulary definitions.
Protocol Vocabulary and Bindings:
  Extensions to protocol vocabulary definitions and protocol bindings.